GSM/GPRS/GPS TRACKER

USER MANUAL

Preface

Thank you for purchasing the GPS tracker This manual shows how to operate the device smoothly and correctly. Make sure to read this manual carefully before using this product. Please note that specification and information are subject to changes without prior notice in this manual. Any change will be integrated in the latest release. The manufacturer assumes no responsibility for any errors or omissions in this document.

Content

1 Summary          ------ ----------------------------------------------------------------------------------     3

2 Application        ------------------------------------------------------------------------------------------     3

3 Hardware description

3.1 Front face  ------------------------------------------------------------------------------------------     3

3.2 Rear face   ------------------------------------------------------------------------------------------     3

3.3 Side face   -------------------------------------------------------------------------------------------    3

3.4 Bottom face -------------------------------------------------------------------------------------------    4

3.5 Interior    -------------------------------------------------------------------------------------------    4

4 Specifications      --------------------------------------------------------------------------------------------    4

5 Usage

5.1   SIM card installation  ---------------------------------------------------------------------------    5

5.2   Battery and Charger  ----------------------------------------------------------------------------    5

5.3   Quick Startup        --------------------------------------------------------------------------     5

5.4   Initialization         ---------------------------------------------------------------------- ----     6

5.5   Change or resume he password  -----------------------------------------------------------------  6

5.6   Authorization        --------------------------------------------------------------------------     6

5.7   Real-time polling     ----------------------------------------------------------------------------    6

5.8   Auto track       -----------------------------------------------------------------------------------   7

5.9   Voice Surveillance     ------------------------------------------------------------------------      7

5.10  Modes switch between “track” and “monitor”  -------------------------------------------      7

5.11  Geo-fence            -----------------------------------------------------------------------       7

5.12  Movement Alert       -----------------------------------------------------------------------       8

5.13  Overspeed Alert       ----------------------------------------------------------------------        8

5.14  IMEI Check          ----------------------------------------------------------------------        8

5.15  SOS Button           --------------------------------------------------------------------         8

5.16  Low battery alert      --------------------------------------------------------------------         8

5.17  Restart the tracker.    --------------------------------------------------------------------         8

5.18  Hidden number tracking       --------------------------------------------------------         9

5.19  SMS center           -------------------------------------------------------- ------------         9

5.20  Set number in a online positioning platform ---------------------------------------------        9

5.21  Modes switch between"telephone "and"web  --------------------------------------------------   9

5.22  GPRS stored function  introduction------------------------------------  10

5.23  GPRS setting       --------------------------------------------------------------------            10

5.24   Set time  ------------------------------------------------------------------------------------

5.25   Shake alarm system   ----------------------------------------------------------------------           10

6 Cautions                      ---------------------------------------------------------------------       10

7 Faults & Solutions              ---------------------------------------------------------------------       11

8Command                   ---------------------------------------------------------------------       12

1 Summary

Working Based on existing GSM/GPRS network and GPS satellites, this product can locate and monitor any remote targets by SMS or GPRS.

2 Applications

- Vehicle rental / Fleet management etc

- Protect child / the old / the disabled / pet etc

- Provide peace-of-mind for businessmen

- Manage personnel

- Track criminals secretly

3 Hardware Description

3.1 Front face                          3.2ce Rear fa

3.3 Side face

`3.4 Bottom face

3.5 Interior

4 Specs.

| Content | Specs. |
| --- | --- |
| Dim. | 64mm x 46mm x 17mm(1.8”*2.5”*0.65”) |
| Weight | 50g |
| Network | GSM/GPRS |
| Band | 850/1800/1900Mhz or 900/1800/1900Mhz or 850/900/1800/1900 |
| GPS chip | SIRF3 chip |
| GSM/GPRS module | Simcom300 or Simcom340 |
| GPS sensitivity | -159dBm |
| GPS accuracy | 5m |
| Time To First Fix | Cold status 45s Warm status 35s Hot status 1s |
| Car charger | 12—24V input 5V output |
| Wall charger | 110－220V input 5V output |
| Battery | Chargeable changeable 3.7V 800mAh Li-ion battery |
| Standby | 48hours |
| Storage Temp. | -40°C to +85°C |
| Operation Temp. | -20°C to +55°C |
| Humidity | 5%--95% non-condensing |

5 Usage

5.1 SIM card installation

Make sure that there is no call transfer and call display is on, and PIN code off. The SMS message must in Text format, can’t be identified for PDU format.

Steps:

1 Open the rear cover, and pick out the battery.

2 Push the foil along and turn it left.

3 Put the SIM card into the holder, and turn the foil right and fasten it in place.

5.2 Battery and Charger

Do charge the battery to capacity in 8 -12 hours for first use. Please use the battery and charger provided by the manufacturer. This unit adopts built-in Li-ion battery, and full battery will support around 48 hours use on end. After first use, the battery can be charged fully in 3-5hours.

Cautions:

a: For it’s Li-ion battery, which contains harmful chemicals and may burst, please don’t bump, puncture it violently and keep it off fire.

b: Please charge the battery in time to keep it working normally.

5.3 Startup

- Put the SIM card and battery in place.

- Turn on the unit outdoors by pressing the “on/off” button until the indicator is on.

- For first use, please initialize the unit and restore it to default setting.( please refer to 5.4 for instruction.)

- In 10 or 40seconds, the unit will begin to work and acquire the GSM signals as well as the GPS signals. The indicator will keep flashing every 4 seconds when the unit has received the signals, otherwise it will keep on.

- When this unit receives GPS signals normally, you can use it and do all the following settings.

5.4 Initialization

Send “begin+password” in SMS to the unit, it will reply “begin ok” and initialize all the settings. (default password: (123456)

5.5 Change the password

Send SMS "password+old password+#+new password "to change the password.

Remark:

5.5.1 Be sure keep the new password in mind, you have to upload the software to restore the original setting in case of losing the new password.

5.5.2 Make sure the new password is in 6 digits, or else the tracker can not recognize the password.

5.5.3  you can Send "resumepassword" to the tracker, to restore the original setting in case of losing the new password,and it will reply resume password,pass word is 123456

5.6 Authorization

There are only 5 numbers able to be authorized.

5.6.1  Call the tracker for 10 times, it will make the cell phone number as the authorized number automatically.

5.6.2  Send SMS "admin+password+#+cell phone number" to set up a authorized number. The other

authorized numbers should be set by the first authorized number. If the number is successfully authorized, th

unit will reply “admin ok!” in SMS.

5.6.3  Send SMS "noadmin+password+#+authorized number" to delete the authorized number.

5.6.4  For roaming purpose, you have to add your country code ahead of the cell phone number, for example, please send admin123456 008613322221111 to tracker to set 13322221111 as an authorized number.

5.7 Real-time polling

5.7.1 If there is no authorized number, when any number dials up the unit, it will report a Geo-info; If there is already an authorized number, then it will not respond when an unauthorized number calls it up.

5.7.2 When an authorized number dials up the unit, it will hang up and report a real-time Geo-info as below:

5.8 Auto Track

Report a Geo-info at 30s intervals to the authorized numbers for 15 times:

5.8.1 Set up: Send SMS "t030s005n"  to the unit, it will report the Geo-info at 30s intervals for 5 times.(s: second, m: minute, h: hour). The setting must be in 3 digits and at maximum 255 in value.

5.8.2 Send SMS"t030s***n+password to the unit,t will report the Geo-info at 30s intervals for the unlimited times

Remark:you can set the time slot by yourself.

5.83 Cancel:" Send "notn+password" to delete the “ auto track ”

Remark: the interval must not be less than 20s.

5.9 Voice Surveillance

In this mode, the user can dial up the unit to monitor the voice (please refer to 5.10 for instruction).

5.10 Modes switch between “track” and “monitor”

5.10.1. The default mode is “track”.

5.10.2. Send SMS "monitor+password" to the unit", and it will reply “monitor ok!” and switch to “monitor”mode.

5.10.3. Send SMS "tracker+password "to the unit, it will reply “tracker ok!” and restore to “track” mode.

5.11 Geo-fence

Set up a geo-fence for the unit to restrict its movements within a district. The unit will send the message to the authorized numbers when it breaches the district.

5.11.1 Set up: When the unit stays immobile in a place for 3-10 minutes, the user can Send SMS "stockade+password+#+geo-info;geo-info " to unit to set the restricted district. In case of breach, it will send SMS “stockade!+geo-info” to the authorized numbers.

Remark : The first longitude& latitude is coordinate of the top left corner of the Geo-fence, while the second longitude&latitude is the coordinate of the bottom right corner. It will alarm at 3minutes intervals for 1 time

5.11.2 Cancel: Send SMS "nostockade+password" to deactivate this function.

This function will be out of effect after the unit moves outside the district.

5.12 Movement alert

5.12.1 Set up: When the unit stays immobile in a place for 3-10 minutes, the user can send SMS "move+password" to the unit, then the unit will reply “move ok!”. In case of such a movement, it will send SMS “Move” along with a Geo-info to the authorized numbers. It will alarm at 3minutes intervals for 1 time.

5.12.2 Cancel: Send SMS "nomove+password" to deactivate the movement alert.

Remark: This function will be out of effect after the unit moves outside the district.

5.13 Overspeed alert:

5.13.1 Set up: Send SMS "speed+password+#+080" to the unit (suppose the speed is 80km/h), and it will reply “speed ok!”. When the target moves exceeding 80 km/h, the unit will send SMS speed+080!+Geo-info to the authorized numbers. at 3minutes intervals for 1 time

5.13.2 Cancel: Send SMS nospeed+password to deactivate the overspeed alert

Remark: It is recommended that the speed alarm is set at not less than 50km/h. For below that rate, it may cause the excursion of the GPS signal influenced by clounds etc.

5.14 IMEI checking:

Send SMS "imei+password "to the unit to check the IMEI number.

5.15 SOS button

Press the SOS for 3 second, it will send “ help me !+ Geo-info” to all the authorized numbers every 3 minutes.

Send the SMS"help me" to the device to cancel the SOS alert,but it will not reply the set ok

5.16 Low battery alert

It begins to alert when it is 3.7V and sends you SMS in 30m interval.

SMS format: low battery+Geo-info.

5.17 Set web

5.17.1 Send SMS："home+password+#+website"   Reply："set home#website"OK

5.17.2：Send SMS "nohome+password" to cancel set web

5.21 Set Web

In order to see your website in each replying SMS ,For example you website is www.webs***.com, then send "home123456 www.webs***.com" . Then it will reply"set home ok",when you want to cancel it, just send "nohome123456",it will reply SMS"cancel home o

5.17 Restart the tracker.

Send SMS "reboot+password" to the tracker. For example“reboot123456”.The tracker will be restarted.

5.18 Hidden number tracking

When a hidden authorized number calls the tracker, the tracker will reply SMS with the hidden number&Geo-info to all the authorized numbers.

5.18.1 Send SMS “hide number” to set up the hidden number.

5.18.2 Send SMS “nohide number” to delete the hidden number.

5.19 SMS center

5.19.1 Send SMS adminsms+password+space+cell phone number to set the SMS center.

If the SMS center is set up, when an authorized number sends SMS to the tracker, the tracker will reply a SMS with Geo-info & authorized number to SMS center.

5.19.2 Send SMS noadminsms+password to cancel the SMS center.

Response SMS format: authorized number+Geo-info

5.20 Set number in a online positioning platform

Add the number on the online positioning platform for tracking. Adding to the special platform, send SMS "number + password+#+tracker number" to the tracker,and will reply set number ok

for example “number 13500001111”. need the platform have the fuction.

5.21Modes switch between “telephone” and “web”

5.21.1 For sending GPS data to IP address:

Set up: Send SMS "web + password" to device.

if set successfully, the device will reply SMS "set web ok".

After this, you can call the tracker. The tracker will hang up the phone and report the GPS data to IP address.

5.21.2  For sending GPS data to telephone:

Set up: Send SMS "telephone + password" to device.

if set successfully, the device will reply ‘set telephone ok’.

And then, the device will send GPS data to your telephone by SMS.

Remark:The default is sending the GPS data to the telephone.

5.22  GPRS stored function  introduction
Put the TF memory card in the device, when the device has no GSM signal, the built-in TF card can store the data distance data, when the device enter into one place which has the GSM signal , the device will feedback the storaged GPRS data to the platform unitl  sending all the storaged GPRS data ,platform to ensure  not lose any GPRS data.

5.23 GPRS setting

In order to use GPRS function, the user needs to set IP, Port and APN ( access point name ) by sending SMS commands.

5.22.1 Set an IP address and port:

Setup: Send SMS"ipport +password+#+IPaddress+，+port number" .If setup successful, the tracker will reply SMS " set ip address and port ok! "

Cancel: Send SMS "noipport+password"

5.22.2 Set APN

Send SMS "apn+password +#+apn"If setup successful, the tracker will reply SMS “APN ok”.

P.S. The old APN will be invalid when you set a new APN.

5.22.3Setup:Send SMS "user+password+#+cmnet+# +cmnet "to set the APN user name and password

As soon as the IP & Port & APN are set up, the user can make a call or send SMS to tracker. The tracker will hand up the telephone and report the coordinates to IP address.

The message sent by tracker to IP address is as following:

Serial number + authorized number + GPRMC + GPS signal indicator + command + IMEI number + CRC16 checksum.

For example, it will send GPS coordinates as below illustrated

5.23 Set Time

In order to make the time as the same with the user country,please send SMS command "time zone+password +#+time zone". For example,if user country time is GMT+8,then send" time zone+password +#++8"to the device. If user country time is GMT-6,then send"zone123456 -6"to device. The device will reply SMS"set time zone ok".

Send SMS "notime zone +password"to cancel time zone

Remark::there is a space between time and zone ,the time zone is 3 digits

5.25  Shake alarm system  (this function can be add or delect for customization )

This function is using for the user to get alarm info someone touchs the unit.Send SMS" shake+password+space+a"device will start up the alarm system ,when the device be touched ,the device will send the alarm to the authorized number and monitor center,send "shake+password+space+b"to cancel the shake alarm system

6 Other settings

Send SMS others+password+#+ABCD           Reply:set others/ABCD ok

Remark:A=0,close device sending reboot sms(default)

A=1,open device sending reboot sms;

B=0,close device "low electricity and auto power off"

B=1,open device " low electricity and auto power off"(default)

C=0,close device enter into blind area(there's no GPS signal) alarm(default)

C=1,open device enter into blind area(there's no GPS signal) alarm

D=0,prohibit system run normally before close all indicators(default)

D=1, make the system run normally before close all indicators

7Cautions

Please comply with the instructions to extend the unit life:

1. Keep the unit dry. Any liquid, i.e. rain, moisture, may destroy or damage the inside circuitry.

2. Don’t use & store the unit in dusty places.

3. Don’t put the unit in overheated or overcooled places.

4. Handle carefully. Don’t vibrate or shake it violently.

5. Clear the unit with a piece of dry cloth. Don’t clean in chemicals, detergent.

6. Don’t paint the unit, this may cause some foreign materials left in between the parts.

7. Don’t disassemble or refit the unit.

8. Please use the battery and charger provided by manufacturer. Using other batteries and chargers will cause unwanted situation.

9. Don’t dismount the antenna randomly, or use other antennas. This may interfere the transmission, and increase the radiation as well.

8Faults & The solutions

| Faults | Solution |
| --- | --- |
| Startup Fail | Check the battery and see if it is fully charged or correctly installed. |
| Hangup Fail | In existence of an authorized number, an unauthorized number dials up the unit. Please initialize the unit and re-set up the authorized numbers. |
| Monitor Fail | Check if the authorized number is setup or in the coverage of signals. |
| Location report in digits of zeros. | Don’t use it in the place beyond reach of signals. Place the unit outdoors, especially when starting it up. |

9 Command

| No | FUNCTION | SMS | SMSREPLY | CHAP |
| --- | --- | --- | --- | --- |
| 1 | Intialition | begin123456 | begin ok | 5.4 |
| 2 | Change password | password123456#666888 | begin123456 | 5.5 |
|  | Resume password | resumepassword | resume password,password is 123456 | 5.5.3 |
| 3 | Add in number | admin123456#13511113333 | admin ok | 5.6.2 |
|  | Delete number | noadmin123456#13511113333 | no admin ok | 5.8.3 |
| 4 | Auto tracking | at30sum15 | auto track set ok | 5.8.1 |
|  | Auto tracking | at30sum0 | auto track set ok | 5.8.2 |
|  | Cancel auto track | noat123456 | cancel auto track ok | 5.8.3 |
| 5 | Monitor mode | monitor123456 | monitor ok | 5.10.2 |
| 6 | Tracking mode | tracker123456 | tracker ok | 5.10.3 |
| 7 | Geo-fence | Stockade123456 geo-info;geo-info | Stockade ok | 5.11.1 |
|  | Cancel geo-fence | nostockade123456 | no stockade ok | 5.11.2 |
| 8 | Movement alert | move123456 | move ok | 5.12.1 |
|  | Cancel movement alert | nomove123456 | cancel move ok | 5.12.2 |
| 9 | Overspeed alert | speed123456#080 | speedok | 5.13.1 |
|  | Cancel overspeed alert | nospeed123456 | cancel speed ok | 5.13.2 |
| 10 | Imei checking | Imei123456 |  | 5.14 |
| 11 | SOS alert |  | help me! | 5.15 |
| 12 | Restart the tracker | reboot123456 |  | 5.17 |
| 13 | Hide number tracking | hide number |  | 5.18.1 |
| 14 | Cancel hide number tracking | Nohide number |  | 5.18.2 |
| 15 | Add number into platform | number13500001111 | set number ok | 5.20 |
| 16 | Web mode | web123456 | set web ok | 5.21.1 |
| 17 | Telephone mode | Telephone123456 | set telephone ok | 5.21.2 |
|  | GPRS setting | ipport123456 220.231.180.37,2332 | set ip address and port ok | 5.22.1 |
| 18 | Set APN | apn123456 #cmnet | set APN ok | 5.22.2 |
| 19 | Set APN user name and password | User123456#cmnet#cmnet |  | 5.22.3 |
| 20 | Set time | TimeZone123456#time zone | Set time zone ok | 5.23 |

# Text boxes

Indicator for signals.

You can update software, charge battery from here.

You can press the “SOS” buttons for 3s for emergent help.

Turn on / off the unit here.

Microphone

GSM/GPRS antenna is inside

Install the battery like this

Put SIM card here.